## Slide 1: Perception for Autonomous Vehicles
Nicolò Parisi

## Slide 2: LANE DETECTION
Process of identifying and tracking road lane markings in real-time
Goal: Enhances safety and navigation in advanced driver-assistance systems (ADAS)
Utilizes images streams captured by onboard cameras or sensors
Generates a clear representation of lane positions to guide vehicle control.
Challenges: Works under varying lighting, weather conditions, and occlusions
Applications: Lane keeping, automated lane changes, and collision avoidance systems.

## Slide 3: MODELS TYPE
Top-down
- Global understanding of the road scene.
- High-level contextual information to predict lane positions.
- Pre-trained models
Bottom-up
- Processing of pixel-level details
- Detecting small-scale features such as edges, colors
- Edge detectors, pixel gradient calculus, statistical distribution

## Slide 4: CANNY EDGE DETECTOR
What is an edge?
Significant and sharp change in the intensity or brightness of an image
4 steps:

## Slide 5: DENOISING
Gaussian filter
Noise in images can cause sudden intensity changes
Smooth intensity gradient changes
σ increase the the blur

## Slide 6: GRADIENT COMPUTATION
- SOBEL ALGORITHM
- convolutional filters
- magnitude of the gradients
- rotation of the edges

## Slide 7: NMS
Pixel with non maximum value in the direction of the edge are discarded.
This produce thinner and more accurate edges

## Slide 8: DOUBLE THRESHOLDING
- Define two thresholds
- strong edge: gradient magnitude above the high threshold -> just retained
- Non-edge: gradient magnitude below the low threshold -> simply discard
- Weak edge: gradient magnitude between the high and low threshold -> conditionally retained if connected to a strong edge
A: strong B: strong C: weak (promoted) E: weak (discard) D: non edge

## Slide 9: HOUGH TRANSFORM
Algorithm introduced 1962 to identify simple shapes in binary images such as:
- lines
- circles
takes in input the output of an edge detector
fills the gaps between them if they exist

## Slide 10: HOUGH TRANSFORM LINES
- Parsing of each pixels of the image
- Line representation:
p = x cos(θ) + y sin(θ)
- Accumulation space

## Slide 11: HOUGH TRANSFORM CIRCLES
- Parsing of each pixels of the image
- For each point on the edges, a circle is drawn with a given radius
- Accumulation space

## Slide 12: HOUGH TRANSFORM PARAMETERS
LINES
- p/θ: resolution of the accumulator.
- Threshold: The minimum number of intersections required to consider a line as detected.
- Min/Max line length: The minimum and maximum length of a line seg-
ment required to be considered a valid line.
CIRCLES
- Max/min Radius: The smallest/largest radius value that the algorithm will consider when searching for circular structures
- Threshold: The minimum number of intersections required to consider a circle as detected

## Slide 13: HOUGH TRANSFORM EASY TO MESS UP
What we expect:
What we can get:

## Slide 14: PRACTICAL APPLICATION Real-Time Lane Detection and Tracking for Advanced DriverAssistance Systems
Fuzzy Noise Reduction Filter (FNRF)
(ROI) image segmentation
Canny Edge Detector
Hough transform
Tracking mechanism ensures continuity across video frames.

## Slide 15: PAIN POINT Reliability / Consistency
Fnrf filter
Gaussian filter

## Slide 16: NEXT STEPS
Deep learning
- No assumptions
- More generalizable
- More robust
LANE NET
Lane edge proposal network: input image output lane edge proposal map.
Lane line localization network: inferring the location of each lane in the image from edge proposal map

## Slide 17: Thank YOU
Nicolò Parisi